2018 CHEVROLET CORVETTE Z06

FAST FACT

Corvette marks 65 years of production in 2018. Only 300 were built in 1953, each of them Polo White with a red interior.

BASE PRICE 
$80,490 coupe

$84,490 convertible

EPA VEHICLE CLASS

Coupe with removable roof panel or Convertible

NEW FOR 2018

- Carbon 65 Edition available on 3LZ trim. Limited to only 650 vehicles (including Carbon 65 Edition on Grand Sport 3LT trim), each with a unique vehicle identification number. Distinctive package blends visible carbon fiber exterior elements including new carbon fiber spoiler and rear quarter intakes with new Ceramic Matrix Gray exterior color and unique interior appointments, including a carbon fiber-rimmed steering wheel and more

- Two new wheel choices: Black Z06 wheel with yellow stripe and Pearl Nickel Blade-design

- Gray interior available

- HD digital radio standard

- Available Performance Data Recorder/Cosworth Toolbox offers four additional data channels: individual wheel speeds, individual suspension displacements, yaw rate and intake and ambient air temperatures

- Improved rear-view camera image

- Enhanced Head-Up Display rotation setting

- Ceramic Matrix Gray replaces Sterling Blue in the exterior color palette

- Spice Red convertible top

- Spice Red interior offered on 3LT and 3LZ trims

- Jet Black sueded-wrapped interior includes carbon rim steering wheel and gloss carbon fiber interior trim

- New interior color stitching packages (red/yellow/new blue) offered on 3LT and 3LZ trims

VEHICLE HIGHLIGHTS

- Offered in 1LZ, 2LZ and 3LZ trims

- Unique, purposeful exterior components designed to reduce lift – including front splitter – and accommodate cooling requirements for the engine and brakes

- LT4 supercharged 6.2L V8 SAE-certified at 650 hp and 650 lb-ft of torque is the most powerful Corvette production engine ever

- Standard Magnetic Ride Control and Performance Traction Management

- Available Z07 package adds adjustable front and rear aero components for unprecedented aerodynamic downforce, Michelin Pilot Sport Cup 2 tires for enhanced grip, and Brembo carbon ceramic-matrix brake rotors that improve braking performance and contribute to greater handling through reduced unsprung weight

# Z07 package (with available eight-speed automatic) enables 0-60 mph in 2.95 seconds, 10.95-second quarter-mile, lateral acceleration of 1.2g and 60-0 braking in 99.6 feet

- Standard Michelin Pilot Super Sport P285/30ZR19 front tires are 1.5 inches wider than the tires on the Stingray, while the 335/25ZR20 rear tires are two inches wider (Sport Cup 2 tires with Z07 package)

- Five-position Drive Mode Selector that tailors 12 vehicle attributes to fit the driver’s environment

- Interior that offers genuine carbon fiber and aluminum trim, hand-wrapped leather materials and dual eight-inch configurable, high-definition color driver/infotainment screens

- Chevrolet MyLink with 8-inch-diagonal color touchscreen

- Apple CarPlay and Android Auto smartphone projection capability

- Keyless open and start

- Curb-view cameras included on 2LZ and 3LZ trims

- Head-up display is standard

- Bose 10-speaker audio system with bass box included on 2LZ and 3LZ trims

- Heated and ventilated leather-trimmed seats are included on 2LZ and 3LZ trims

- Standard dual-zone automatic climate control

- Corvette Museum delivery and Customer Engine Build Program are available

SAFETY FEATURES

- Four standard air bags, including side-impact air bags

- Four-wheel disc brakes with four-channel ABS

- Active Handling with electronic stability control

- Safety belt pretensioners

- Rear-vision camera

- Tire pressure monitoring with run-flat tires

2018 CHEVROLET CORVETTE Z06

GM-EST. FUEL ECONOMY

| City | 15 mpg (manual) 13 mpg (automatic) |
| --- | --- |
| Highway | 22 mpg (manual) 23 mpg (automatic) |

FUEL TANK CAPACITY

18.5 gal. / 70 liters

ENGINE

| Type: | LT4 6.2L Supercharged V8 with direct injection and Active Fuel Management (cylinder deactivation) |
| --- | --- |
| Bore & stroke (in / mm): | 4.06 x 3.62 / 103.25 x 92 |
| Block material: | Cast aluminum |
| Cylinder head material: | Cast aluminum |
| Valvetrain: | Overhead valve, two valves per cylinder |
| Fuel delivery: | Direct injection |
| Horsepower (hp @ rpm): | 650 @ 6400 rpm (SAE certified) |
| Torque (lb.-ft. @ rpm): | 650 @ 3600 rpm (SAE certified) |

TRANSMISSION & AXLE

| Type: | 7-speed manual with Active Rev Match 8-speed paddle-shaft automatic |
| --- | --- |
| Final Drive Ratio: | 3.42 (manual) 2.41 (automatic) |

CHASSIS & SUSPENSION

| Front Suspension: | Short/long arm (SLA) double wishbone, cast aluminum upper and lower control arms, transverse-mounted composite spring, Magnetic Selective Ride Control |
| --- | --- |
| Rear Suspension: | Short/long arm (SLA) double wishbone, cast aluminum upper and lower control arms, transverse-mounted composite spring, Magnetic Selective Ride Control |
| Steering Type: | Variable-ratio rack-and-pinion with electric power assist |
| Turning Circle (ft. / m): | 37.7 / 11.5 |
| Brake Type: | Front and rear power-assisted discs with two-piece steel rotors; fixed six-piston aluminum front calipers and fixed four-piston aluminum rear calipers; carbon ceramic matrix rotors with Z07 pkg. |
| Brake Rotor Size (in. / mm): | Front – Z06 : 14.6 / 371 Front – Z06 w/Z07: 15.5 / 394 Rear – Z06: 14.4 / 365 Rear – Z06 w/Z07: 15.3 / 388 |
| Wheel Size: | Front: 19-inch x 10-inch Rear: 20-inch x 12-inch |
| Tire Size: | Michelin Pilot Super Sport run-flat (std.) Michelin Pilot Sport Cup 2 (Z07) Front: P285/30ZR19 Rear: P335/25ZR20 |

EXTERIOR DIMENSIONS

| Wheelbase (in. / mm): | 106.7 / 2710 |
| --- | --- |
| Overall Length (in. / mm): | 176.9 / 4493 |
| Overall Width (in. / mm): | 77.4 / 1965 |
| Overall Height (in. / mm): | 48.6 / 1234 (coupe) 48.7 / 1237 (convertible) |
| Track (in. mm): | 63.5 / 1613 (front) 62.5 / 1588 (rear) |

INTERIOR DIMENSIONS

| Headroom (in. / mm): | 38 / 962 |
| --- | --- |
| Legroom (in. / mm): | 43 / 1092 |
| Shoulder Room (in. / mm): | 55 / 1397 |
| Hip Room (in. / mm): | 54 / 1371 |

WEIGHTS & CAPACITIES

| Curb Weight (lb. / kg): | 3524 / 1598 (coupe) 3582 / 1625 (convertible) |
| --- | --- |
| EPA passenger volume (cu. ft. / L): | 52 / 1472 |
| Cargo volume (cu. ft. / L): | 15 / 425 (coupe) 10 / 283 (convertible) |