SPYKER C8 AILERON

Body style

Two-door, two-seater mid-engined sports coupe. All-aluminium spaceframe chassis

composed of extrusions and folded sheet aluminium, with ‘superformed’ aluminium body

panels. Extruded aluminum side-impact bars and integral rollover bars. Xenon headlights

with LED sidelights and indicators. LED taillights. Longitudinally-mounted V8 engined driving

the rear wheels via a six-speed automatic transmission with paddle controls.

Engine

Type Normally aspirated 90 degree V8 with VVT

Capacity 4.2-litre, 4172 cc

Bore & Stroke 84.5 x 93.0 mm

Compression ratio 11.0:1

Max power 400 ps (298 Kw) @ 6800 rpm

Max torque 480 Nm (354 lb ft) @ 3500 rpm

Max revolutions 7200 rpm

Valves 40 (5-per-cylinder)

Fuel system Multi-point fuel injection

Exhaust system Stainless steel with active bypass valves

Drivetrain & Transmission

Transmission Rear-mounted ZF Tiptronic 6-speed automatic

Type Torque converter with fully auto and sport/semi-auto modes

Gear shift Steering wheel-mounted paddle shift controls

Suspension

Fully independent system co-developed with Lotus Engineering

Front Forged aluminium double wishbones, with new kinematic layout,

Bilstein mono-tube dampers, Eibach coil over damper steel springs

and anti-roll bar

Optional KW hydraulic ride height elevation system (40mm)

Rear Forged aluminium double wishbones, with new kinematic layout,

Bilstein mono-tube dampers, Eibach coil over damper steel springs

and anti-roll bar

Steering

Type Servotronic speed-sensitive hydraulic power assisted rack & pinion

Gearing 3.0 turns of steering wheel lock-to-lock

Brakes

Front 350 mm diameter vented and cross-drilled steel discs with four-piston

AP Racing brake calipers and Ferodo DS2500 high performance pads

Rear 332 mm diameter vented and cross-drilled steel discs with four-piston

AP Racing brake calipers and Ferodo DS2500 high performance pads

Balance Default setting 60/40% front/rear balance

Safety Aids Anti-lock Braking System (ABS)

Electronic Brake Distribution (EBD)

Wheels

Standard

Front 8.5J x 19 in Bright Silver in alloy wheels

Rear 10.0J x 19 in Bright Silver in alloy wheels

Optional*

Front Rotorblade™ 10-spoke 8.5J x 19 in forged alloy wheels

Rear Rotorblade™ 10-spoke 10.0J x 19 in forged alloy wheels

*available in choice of 4 finishes

Tyres

(For fitment to both Standard and Optional wheels)

Front 235 / 35 ZR19

Rear 295 / 30 ZR19

DIMENSIONS

Length 4590 mm 180.7 in

Width 1950 mm 77.0 in (excluding mirrors)

Height 1270 mm 50.0 in

Wheelbase 2725 mm 107.2 in

Front track 1625 mm 64.0 in

Rear track 1645 mm 64.8 in

Weights & Capacities

Kerb weight 1425 kg 3142 lbs

Fuel tank 57 litres 15 gallons (US)

Luggage capacity 120 litres

Performance

Acceleration 0-100 kph (62 mph) – 4.5 seconds

Max speed 300 kph (186 mph)

Optional Compressor

Upgrade Engine 500 HP

***********************